## Slide 1
Digital Logic Design and Application
Topic 2 - Principles for digital design Yan Bo
School of Information & Communication Engineering, UESTC
Email: yanboyu@uestc.edu.cn

## Slide 2: Topic2： Principles for digital design
Combinational Logic
Sequential Logic
Testbench
Gates and Logic
DFF/Latch, Register & Memory
State machine Description
Design & Analysis
Design & Analysis
Function Description
Response Monitor
Test module
Stimulus Generator

## Slide 3: Topic2： Principles for digital design
Combinational Logic
Sequential Logic
Testbench
Gates and Logic
DFF/Latch, Register & Memory
State machine Description
Design & Analysis
Design & Analysis
Function Description
Response Monitor
Test module
Stimulus Generator

## Slide 4: Where we are
TEST
Central Process Unit
Controller
(State Machine)
Datapath
(ALU, MUX…)
Boolean Algebra
Gates
Combinational Circuit
Sequential
Circuit
Central Process Unit
Datapath
(ALU, MUX…)
Controller
(State Machine)
TEST
Boolean Algebra
Sequential
Circuit
Topic2-1
Chap
2&3&4
Chap1
Chap1

## Slide 5: Organization of Center Processor Unit
2026-03-21
P65

## Slide 6: Topic2： Principles for digital design
Combinational Logic
Sequential Logic
Testbench
Gates and Logic
DFF/Latch, Register & Memory
State machine Description
Design & Analysis
Design & Analysis
Function Description
Response Monitor
Test module
Stimulus Generator

## Slide 7: Gates and Logic: basic gates
Gates: A Device executes Boolean Operation
（a）AND gate （b）OR gate （c）NOT gate or Inverter
Chap2.5

## Slide 8: Gates and Logic: other gates
N
N
N
N
Q1: Could you write out any other gates?
Q2: Could you recognize the gates with same function?
Q3: Do we need to fabricate all types of gates?
XN
X
XN

## Slide 9
Gates and Logic: complete Set of Gates
  A set is COMPLETE
    if we can implement any logical function using only the type of gates in the set.
  Minimal Complete set
    A complete set with no redundant elements.
  Examples
  {AND, OR, NOT}
  {OR, NOT}
  {NAND}
  {NOR}
Not a minimal complete set
Simplest and Lowest Cost

## Slide 10: Gates and Logic: NAND as a Complete Set
Proving NAND gate is universal:
Inverter is the most basic and cheapest component.
How can we achieve the basic logic operations only by NAND gate?

## Slide 11
Gates and Logic: Circle rule
P38 Figure2.10 13a，13b DeMorgan’s laws
Basic Forms of Logic Function
  OR-AND-NOT ，AND-OR-NOT
  NAND-NAND， NOR-NOR
  Minimal complete set
(A+B)(A+C)’
(AB+AC)’

## Slide 12
Please use the NOR-gates to replace all gates.
Double inversion cancels
‘
complemented input cancels inversion
Step 1: replace all OR gates by NOR gates;
Step 2: replace all AND gates by NOR gates;
‘
Gates and Logic: Circle rule
P38 Double Complement 8a
DeMorgan’s laws 13a，13b

## Slide 13
Please use the Nand-gates to replace all gates
Bobbles cancels
‘
Add inverter
Step 1: replace all AND gates by NAND gates;
Step 2: replace all ORgates by NAND gates;
‘
Gates and Logic: Circle rule
Chap3.2.1
P38 Double Complement 8a
DeMorgan’s laws 13a，13b

## Slide 14
Please give the Nand-Nand logic diagram and expression for the following circuit.
Exercise

## Slide 15
F (X,Y,Z ) =
X
Y
F
Z
Logic expression
X
Y
Z
F
Exercise
Switch X/Y/Z: 1-Close,0-Open
Lamp F: 1-ON,0-OFF
Logic circuit
Truth table
X·(Y+Z)
X
Y
Z
F
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
0
0
1
1
1
Chap2.3&2.4

## Slide 16: Exercise
A
B
Z
Please write down the truth table, logic expression and the logic symbol of these electronic circuit.
A
B
Z
A
Z
R
Produce a 1 output if and only if all of its inputs are 1.
A
B
Z
Produce a 1 if and only if one or more of its input are 1.
A
B
Z
Z = A + B
Z = A · B
Produce an output value that is the opposite of its input value.
Z = A’
A
Z
Switch/Lamp: 1-Close/ON, 0-Open/OFF
How about this situation: 0-Close/ON, 1-Open/OFF

## Slide 17: Exercise
A
B
Z
Please write down the truth table, logic expression and the logic symbol of these electronic circuit.
A
B
Z
A
Z
R
A
B
Z
A
B
Z
A
Z
1-Open/OFF,0-Close/ON
Switch/Lamp
1- Close/ON,0-Open/OFF
Positive logic
Negative logic
A
B
Z
A
B
Z
A
Z
A’
B’
Z’
A’
B’
Z’
A’
Z’

## Slide 18: Gates and Logic: Positive Logic vs. Negative Logic
Positive logic
Negative logic
  ANDOR
FD (X1 , X2 , … , Xn )
Duality expression
Chap4.1

## Slide 19: Gates and Logic: Principle of Duality
Dual of a logic expression
FD(X1 , X2 , … , Xn ,0,1, + , · )= F(X1 , X2 , … , Xn ,1,0, · , + )
Rule for Duality expression
  AND  OR；
  0  1
  Keep the operation order of the original function
Principle of Duality
  If F1=F2, then F1D=F2D.
X is not changed !!
Chap2.7.2

## Slide 20: Gates and Logic: Perform the dualities
F2 = X + Y · (Z + W)
F2D = X·(Y+Z ·W)
F3D= ((X’+Y ·Z’ ) · ( Z · W)’)’
F3 = ( X’·(Y+Z’) + (Z+W)’ )’
F1 = X + X · Y
F1D= X X Y
= X + Y
= X (1+Y)
Wrong!
F1D= X·(X + Y)
= X
·
+
= X
= F1D
Defination:
F3’ = X’·(Y+Z’) +(Z + W)’
= ((X+ Y’·Z ) · (Z’ · W’)’ )’
DeMogan’s law:

## Slide 21: Gates and Logic: Duality vs. DeMorgan’s Law
Dual of a logic expression
FD(X1 , X2 , … , Xn ,0,1, + , · )
= F(X1 , X2 , … , Xn ,1,0, · , + )
Complement of a logic expression
F’ (X1 , X2 , … , Xn ,0,1, + , · )
= F(X1 ’ , X2 ’ , … , Xn ’ ,1,0, · , + )
X is not changed !!
X is inverted !!
FD(X1 ’ , X2 ’ , … , Xn ’ ,0,1, + , · )=F’ (X1 , X2 , … , Xn ,0,1, + , · )
F(X1 , X2 , … , Xn)=(F’ (X1 , X2 , … , Xn ))’=(FD(X1 ’ , X2 ’ , … , Xn ’ ))’
Chap2.7.2，2.7.3

## Slide 22: Exercise
  Please give the Dual function and the Inverse function for F(a,b,c)=a + bc, and then draw the logic circuit.
  F’(a,b,c)
  =a’ (bc)’
  =a’ (b’+c’)
  FD(a,b,c)
  =a (b+c)
=FD(a’,b’,c’ )
Duality
DeMorgan’s law
a
b
c
F(a,b,c)
a
b
FD(a,b,c)
c
FD(a’,b’,c’)
a'
b'
c'
=(a+bc)’
a
b
c
F’(a,b,c)
a
b
c
F’(a,b,c)
F’(a,b,c)
a
b
c
F’(a,b,c)

## Slide 23: Topic2： Principles for digital design
Combinational Logic
Sequential Logic
Testbench
Gates and Logic
DFF/Latch, Register & Memory
State machine Description
Design & Analysis
Function Description
Response Monitor
Test module
Stimulus Generator
Design & Analysis

## Slide 24: Description for Combinational Circuit
which adds 2 binary digits (X,Y) and a carry(Cin) to give a sum(Sum) and a carry out(Cout) .
Full adder
Truth table
X Y Cin Cout Sum
Input
Output
Logical expression
Cout= X’YCin + XY’Cin + XYCin’ + XYCin
Sum=(X+Y+Cin) (X+Y’+Cin’) (X’+Y+Cin’) (X’+Y’+Cin）
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 1
0
1 0
1 1
0 0
0 1
1 0
0 1
Logic Symbol
Row#
0
1
2
3
4
5
6
7
=∑(3,5,6,7)
=∏(0,3,5,6)
SOP (Sum of Products)
POS(Products of Sum)
Summary for getting SOP from truth table:
Get an AND-OR expression by adding some products;
Each product come from one input combination which make the output is “1”;
For the input combination, using original signal for ‘1’ and complemented signal for “0”;
Summary for getting POS from truth table:
Get an OR-AND expression by multiplying some sums;
Each sum come from one input combination which make the output is “0”;
For the input combination, using original signal for ‘0’ and complemented signal for “1”;

## Slide 25: Description for Combinational Circuit
which adds 2 binary digits (X,Y) and a carry(Cin) to give a sum(Sum) and a carry out(Cout) .
Full adder
Truth table
X Y Cin Cout Sum
Input
Output
Logical expression
Cout= X’YCin + XY’Cin + XYCin’ + XYCin
Sum=(X+Y+Cin) (X+Y’+Cin’) (X’+Y+Cin’) (X’+Y’+Cin）
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0 1
0
1 0
1 1
0 0
0 1
1 0
0 1
Logic Symbol
Row#
0
1
2
3
4
5
6
7
=∑(3,5,6,7)
=∏(0,3,5,6)
SOP (Sum of Products)
POS(Products of Sum)
Cin
XY
00 01 11 10
0
1
1
Cout
1
1
1
0
0
0
0
Cin
XY
00 01 11 10
0
1
1
Sum
1
1
1
0
0
0
0
  Karnaugh map
Input
Output
  Verilog code
module (
output reg ,
input
);
always @ （ ）
begin
end
endmodule
Fulladder
X,Y,Cin
Cout,Sum
Sum=X ^ Y ^ Cin;
Cout=(X&Y) | (Cin& (X^Y));
X,Y,Cin

## Slide 26
Conversions between different representations
Logic expression

Truth table / K map
Truth table / K map

Logic expression
Chap2.6
Chap3.3.2

## Slide 27
Logic expression  Truth table / K map
F(X,Y,Z) = X + Y’Z + X’YZ’
X
Y
Z
F
SOP(Sum-of-Products)
“AND-OR”
Y’·Z
X’·Y·Z’
1
1
0
0
0
0
1
0
0
1
1
1
1
1
1
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
0
0
0
0
0
0
0
0
0
0
0
0
0
1
1
1
1
Z
XY
00
1
0
1
01
11
10
F
Gray code
0
0
1
1
1
1
1

## Slide 28
Logic expression  Truth table / K map
F (X,Y,Z)= (Y’+Z) · (X’+Y+Z’)
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
X
Y
Z
Y’+Z
X’+Y+Z’
F
POS(Product-of-sums)
OR-AND
1
1
1
1
0
0
1
1
1
1
1
1
1
0
0
0
0
1
1
1
1
1
1
1
Z
XY
00
1
0
1
01
11
10
F
Gray code
0
0
1
1
1
1
0

## Slide 29
Truth table / K map  Logic expression
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
X
Y
Z
F
F(X,Y,Z) = + +
SOP/AND-OR
Z
XY
00
0
1
01
11
10
F
0
1
1
1
0
0
0
0
0
0
0
0
0
1
1
1
X’YZ
XY’Z
XYZ’
28
F(X,Y,Z) =( )( )( ) ( )( )
X’YZ
XY’Z
XYZ’
POS/OR-AND
X+Y+Z
X+Y+Z’
X+Y’+Z
X’+Y+Z
X’+Y’ +Z’
X+Y+Z
X+Y+Z’
X+Y’+Z
X’+Y+Z
X’+Y’ +Z’
more simple
= Sx,y,z (3,5,6)
= ∏x,y,z (0,1,2,4,7)
0
1
2
3
4
5
6
7

## Slide 30
Truth table / K map  Logic expression
0 0 0 1
0 0 1 1
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 1
X
Y
Z
F
Z
XY
00
0
1
01
11
10
1
1
1
0
0
F
1
1
1
X’Y’Z’
X’+Y+Z
X+Y’+Z
F(X,Y,Z) = + + + + +
SOP/AND-OR
F(X,Y,Z) =( )( )
X’Y’Z’
X’Y’Z
X’YZ
POS/OR-AND
X+Y’+Z
X’+Y+Z
more simple
X’Y’Z
X’YZ
XY’Z
XYZ’
XYZ
XY’Z
XYZ’
XYZ
= Sx,y,z (0,1,3,5,6,7)
= ∏x,y,z (2,4)
0
1
2
3
4
5
6
7

## Slide 31
Conversions between different representations
Logic expression

Truth table / K map
Logic/Gates circuit
Truth table / K map
Logic/Gates circuit


Logic expression
Logic expression
Logic expression

Chap2.10

## Slide 32
Logic circuit  Logic expression
F =( (A+B)’+(A’+B’)’)’
(A’+B’)’
(A+B)’
A
B
B’
A’
=(A+B)(A’+B’)
=AB’+A’B
=AB
Simplify
13 DeMorgan’s
8 Double Complement
P38 laws&theorems
12 Distributive laws
9 Inverse
Definition of XOR gate
  Please build an XOR only with NOR gates.

## Slide 33
Logic expression  Logic circuit
F=(A+B’C)’+A’BC’+C
A’BC’
B’C
A+B’C

## Slide 34: Exercise
Row X Y Z F
0 0 0 0 1
1 0 0 1 0
2 0 1 0 0
3 0 1 1 1
4 1 0 0 1
5 1 0 1 0
6 1 1 0 1
7 1 1 1 1
Truth table
Please give the
K-map,
SOP expression and circuit,
POS expression and circuit,
according to the truth table.
Z
XY
00
0
1
01
11
10
F
1
1
0
1
1
0
0
1
FSOP = X’Y’Z’ + X’YZ + XY’Z’ + XYZ’ +XYZ
FPOS =(X+Y+Z’)(X+Y’+Z)(X’+Y+Z’)
= Sx,y,z (0, 3,4,6,7)
= ∏x,y,z (1,2,5)

## Slide 35
Conversions between different representations
Logic expression

Truth table / K map
Logic/Gates circuit
Truth table / K map
Logic/Gates circuit


Logic expression
Logic expression
Logic expression

Logic expression

Other logic expression

## Slide 36
  Standard representations
Minterm is a product term in which all the variables appear exactly once either complemented or uncomplemented.
Maxterm is a sum term in which all the variables appear exactly once either complemented or uncomplemented.
Canonical sum of Products (canonical SOP):
A sum of the minterms corresponding to truth-table rows for which the function produces a 1 output.
  Canonical product of Sums(canonical POS)
  A product of the maxterms corresponding to truth-table rows for which the function produces a 0 output.
ex) "Normal " ABC A + B' +C ex) "Non-Normal" ABB' A + A'
Normal Term is a term in which no variable appears more than once.
  Simplify representations
ex) ABC AB‘C A’B‘C
ex) A+B+C A+B‘+C A’+B‘+C
ex) F(A,B,C) = A‘BC’ + ABC‘ + A’BC
ex) F(A,B,C) =(A+B+C)(A+B+C')(A'+B+C)
Use the non-normal term to minimize the cost of realizing a logical function.
Logic expression  other Logic expression
Chap2.8，2.9

## Slide 37
Minterm vs. Maxterm & Canonical SOP vs. POS
Given F(A,B,C )=C’, please construct the truth table and express in both maxterm and minterm form.
In genaral , the relationship between minterm mi and maxterm Mi is:
  F(A,B,C) = M1M3M5M7 = PABC(1,3,5,7)
  =m0+m2+m4+m6 = SABC(0,2,4,6)
m0
m2
m4
m6
M1
M3
M5
M7
0
0
0
0
1
1
1
1
  (mi)' = Mi
= (A+B+C ')(A+B '+C')(A '+B+C')(A'+B '+C‘)
= A’B’C’ + A’BC’ + AB’C’ + ABC’
How about the relationship between the CSOP and the CPOS for a same logic function?
  Ex:
  m0 = A’B’C’, M0 = A+B+C
  m1 = A’B’C, M1 = A+B+C’
  m5 = AB’C, M5 = A’+B+C’
  ………

## Slide 38
0 0 0 0
0 0 1 0
0 1 0 0
0 1 1 1
1 0 0 0
1 0 1 1
1 1 0 1
1 1 1 0
X
Y
Z
F
Minterm vs. Maxterm & Canonical SOP vs. POS
1
1
1
0
1
0
0
1
F’
FD
1
0
1
2
3
4
5
6
7
1
1
1
0
0
1
0
For F  F’, Do: ΣΠ and j=i
For F  FD , Do: ΣΠ and j=n-i
For FSOP FPOS , Do: ΣΠ and j≠i
m5=X·Y’·Z M5=X’+Y+Z’
m6= X·Y·Z’ M6= X’+Y’+Z
m3=X’·Y·Z M3= X+Y’+Z’

## Slide 39
If
write: (1) The canonical product of F1 , F1’ and FD
(2) The standard representation of F=F1+F2
(3) The standard representation of G=F1·F2
union
intersection
  F1D = Pwxyz (14, 10, 8, 6, 2)
Exercise

## Slide 40
Logic expression simplify
Six standard representations for any logic function:
Simplification Goal
  minimize the cost of realizing a logical function
Cost measures and other considerations
  Number of gates
  Number of cascade levels
  Gate fan in and/or fan out
  Interconnection complexity
Two-level realizations
  Minimize the number of gates (terms in logical function)
  Minimize the fan in (literals in logical function)
True table/K map, canonical SOP/minterm list, canonical POS/maxterm list
  Formula Method
  K Map Method
  Other Math Method

## Slide 41
Logic expression simplify by manual:
Formula Method depending on the laws
Simplification theorems:
Combining Method： XY+XY’=X(Y+Y’)=X
Covering Method： X+XY=X(1+Y)=X
Remove literal Method： X+X’Y = X+Y
Idempotent laws: X+X=X
Inverse Laws : X+X’=1
Consensus theorem: XY+X’Z+YZ = XY+X’Z
P38 the laws
Could you write out the other expression of Dual pair?
40

## Slide 42
= Y’ + Z·W
F1 = X·Y’ + X·Z·W + X’·Y’ + X’·Z·W
Logic expression simplify by manual:
Formula Method depending on the laws
F2 = X·Y + X·Y·Z’ + X·Y·W + X·Y·Z·W’
= X·Y·( 1 + Z’ + W + Z·W’ )
= X·Y
X·Y+X·Y’=X
X+X·Y = X
F3=AC+B’C+BD’+CD’+A(B+C’)+A’BCD’+AB’DE
=AC+B’C+BD’ +A(B’C)’ +AB’DE
=A+B’C+BD’
XY+X’Z+YZ=XY+X’Z
X+X’Y=X+Y
X+XY=X
So difficult~~~~~

## Slide 43
Karnaugh map (K-map) is a convenient tool for representing logical functions of three to five variables.
Logic functions are mapped (or plotted) by placing the function’s value (0,1,d ) in each cell of the map.
K-map cells are arranged such that adjacent cells correspond to truth table rows that differ in only one bit position (logical adjacency).
K-maps form the basis of useful heuristics for finding MSOP and MPOS representations by combining cells.
K-map Minimization Steps
Logic expression simplify by manual : K map Method
Draw maps
Circle 1-cells or 0-cells
Read maps
Minimal SOP
Canonical SOP
Chap3.3.2

## Slide 44
Step1：Draw Karnaugh Map
m0
m2
m6
m4
m1
m3
m7
m5
Row0
Row2
Row6
Row4
Row1
Row3
Row7
Row5
Z
XY
00 01 11 10
0
1
YZ
WX
00
00
01
11
10
01
11
10
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11
Put the Truth Table Row number (the minterm number ) so we can copy the Truth Table values into the K-map straight-forward.
Gray code
Be careful the order of the variables

## Slide 45
Two logical adjacent cells can be used to cancel one literal.
1
1
1
1
1
1
Z
XY
00 01 11 10
0
1
YZ
WX
00
00
01
11
10
01
11
10
1
1
1
1
1
1
1
1
XYZ’+ XYZ = XY
X’Y’Z + XY’Z = Y’Z
Step2：Circle logical adjacent 1-cells
X’Y’Z’+X’YZ’=X’Z’
YZ
WX
00
00
01
11
10
01
11
10
1
1
1
1
1
1
1
1
4 items
5 items

## Slide 46
XY
ZW
00 01 11 10
00
01
11
10
1
1
1
1
1
1
1
1
Z
XY
00 01 11 10
0
1
1 1 1 1
1 1
Step3: Read maps
Four logical adjacent cells can be used to cancel 2 literals.
Z’
Y’
YW
Y’W’
F(X,Y,Z) = Y’+Z’
= XYZ (0,1,2,4,5,6)
F(X,Y,Z,W) = YW+Y’W’
= XYZW (0,2,5,7,8,10,13,15)
Be careful the order of the variables
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11
0
4
1
5
3
7
2
6

## Slide 47
Draw maps
Circle cells
Read maps
XY
ZW
00 01 11 10
00
01
11
10
F = XYZ+XYW+XZ’W+Z’W’+XY’Z+X’ZW’
Eight logical adjacent cells can be used to cancel 3 literals.
X
W’
Logic expression simplify by manual : K map Method
1
1
1
1
1
1
1
1
1
1
1
1
F = X+W’

## Slide 48
F = (X,Y,Z,W) ( 0, 2, 3, 5, 7, 8, 10, 11, 13)
XY
ZW
00 01 11 10
00
01
11
10
X’·Y·W
YZ’W
Y’Z
Y’W’
F = Y’Z+Y’W’ +X’YW+YZ’W
Logic expression simplify by manual : K map Method
Draw maps
Circle cells
Read maps
Be careful the order of the variables
1
1
1
1
1
1
1
1
1
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11

## Slide 49
Logic expression simplify by manual: K map Method
The basic rules may include:
The number of cells in a cube must be power-of-2. In general, we can circle rectangular sets of 2i 1-cells to form a product term containing n-i literals.
The cubes must be as large as possible.
The cubes must be as few as possible.
All of the 1-cells need to be circled;
Each cube must cover one or more distinguished 1-cells which covered by only one circle;
……
Actually we have some other precise mathematical methods to determine how to combine and remove redundant literals and gates. And fortunately these methods could be implemented by computer ------ EDA tools.
P83

## Slide 50
Minimizing the following function:
F(A,B,C,D) = m(0,2,3,4,6,7,8,10,11)
AB
CD
00 01 11 10
00
01
11
10
A’D’
A’C
B’C
B’D’
1
1
1
1
1
1
1
1
1
Could you simplify it by formula method?
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11
Exercise

## Slide 51
TRUE
FALSE more cycles
FALSE
the circle can be enlarged
TRUE
F=BC+A’B’C’+A’C’D+A’CD’
F=BC+A’C’D+A’B’D’
F=B+A’B’C
F=B+A’C
Example 1
Example 2
Logic expression simplify by manual : K map Method

## Slide 52
TRUE
TRUE
FALSE
dummy circle
Example 3
Example 4
F=C’+BCD’
F=C’+BD’
F=BD+ABC’+A’C’D+A’BC+ACD
F=ABC’+A’C’D+A’BC+ACD
Logic expression simplify by manual : K map Method
FALSE
the circle can be enlarged

## Slide 53
ZW
XY
00 01 11 10
00
01
11
10
0
0
0
0
0
0
0
X’+Y
X’+Z
F (X,Y,Z,W)= (X+Y’+Z’+W)·(X’+Z)·(X’+Y)
Logic expression simplify by manual : K map Method
Minimize POS
How about to circle 0-cells?
Draw maps
Circle cells
Read maps
X+Y’+Z’+W

## Slide 54
CD
AB
00 01 11 10
00
01
11
10
A’BD
F = B’D’+A’BD+C
Logic expression simplify by manual : K map Method
How about the ‘Don’t care’?
Draw maps
Circle cells
Read maps
C
Use d as you want
F = ABCD( 0, 2, 3, 5,6, 7, 8, 10, 11)+ d ( 14, 15)
d
d
B’D’
1
1
1
1
1
1
1
1
1
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11

## Slide 55
Logic expression simplify by manual : K map Method
Minimizing the following function with Don’t Cares
F(A,B,C,D) = m(1,3,4,7,11) + d(5,12,13,14,15)
CD
AB
00 01 11 10
00
01
11
10
CD
AB
00 01 11 10
00
01
11
10
d
d
d
d
d
F=(A’+C)(C’+D)(B+D)
F= A’·D+C·D+B·C’
MSOP
MPOS
1
1
1
1
1
d
d
d
d
d
0
0
0
0
0
0
EDA tools~~
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11

## Slide 56
CD
AB
00 01 11 10
00
01
11
10
Minimizing the following function with Don’t Cares
F(A,B,C,D) = A’B + B’C + BC’D+ d(14,15)
A’B
F = A’B+BD+C
C
d
d
1
1
1
1
1
1
1
1
1
BD
Exercise

## Slide 57: Summary
  Basic gates & laws
  Minimal Complete set (Circle rule)
  Positive Logic vs. Negative Logic
  Dual (FD) vs. Complement (F’)
  Minterm vs. Maxterm
  The methods for describing logic circuit
  Logic circuit simplify (Formula, K-map )

## Slide 58: Topic2： Principles for digital design
Combinational Logic
Sequential Logic
Testbench
Gates and Logic
DFF/Latch, Register & Memory
State machine Description
Design & Analysis
Design & Analysis
Function Description
Response Monitor
Test module
Stimulus Generator

## Slide 59
Design & Analysis of Combinational Circuits
  Digital Circuit Design is:
  To descript and simplify the function
    truth table/ K map
    logical algebra expressions/equations
    CSOP/Minterm list, CPOS/Maxterm list, MSOP, MPOS
    circuit diagram (Schematic at Module level, RTL level, etc. )
    timing diagram (Waveform)
    Hardware Description Language code (VHDL, Verilog, etc.)
  To realize the hardware
    gates or other devices
    Programmable Logic Devices
    Application Special Integrate Circuit
Digital Circuit Analysis is:
  To determine the behavior of the circuit
  To verify the correctness of the circuit
  To assist in converting the circuit to a different form
Chap3.2，3.3
Chap3.1

## Slide 60: Combinational Digital Circuit Design
2.Truth table
A B C F
0 0 0
0 0 1
0 1 0
0 1 1
1 0 0
1 0 1
1 1 0
1 1 1
  1.Description: 3-input Majority function, which output is 1 whenever majority of inputs is 1.
1
1
1
1
0
0
0
0
0
C
AB
00 01 11 10
0
1
3.K map
0
0
0
1
1
1
1
4.Logical expression
F = AB + BC + AC
5.Circuit schematic

## Slide 61
Combinational Circuits Analysis
  Find a simplified logic for the following circuit :
2.Logical expression
1.Circuit schematic
ABC
A+B+C
AB+BC+AC
F2=AB+BC+AC
F1=ABC+(A+B+C)(AB+BC+AC)’
A | B | C | F1 | F2
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 0 | 1
1 | 1 | 1 | 1 | 1
3. Truth table
0
C
AB
00 01 11 10
0
1
4. K map
1
1
1
0
1
0
0
F1
0
C
AB
00 01 11 10
0
1
0
0
0
1
1
1
1
F2
F2=AB+BC+AC
F1=ABC+A’B’C+A’BC’+AB’C’
5.Description: What’s the circuit’s function?
Parity Generator/Checkers
（Even Checker）
Majority circuit

## Slide 62
Design & Analysis of Combinational Circuits
  Digital Circuit Design is:
  To descript and simplify the function
    truth table/ K map
    logical algebra expressions/equations
    CSOP/Minterm list, CPOS/Maxterm list, MSOP, MPOS
    circuit diagram (Schematic at Module level, RTL level, etc. )
    timing diagram (Waveform)
    Hardware Description Language code (VHDL, Verilog, etc.)
  To realize the hardware
    gates or other devices
    Programmable Logic Devices
    Application Special Integrate Circuit
Digital Circuit Analysis is:
  To determine the behavior of the circuit
  To verify the correctness of the circuit
  To assist in converting the circuit to a different form

## Slide 63: Examples for Combinational Digital Circuit Design
Multiplexer/Demultiplexer
Decoder/ Encoder
Parity Generator/Checker
Operator
Chap1.3，1.4，4.2
2026-03-21

## Slide 64: Multiplexer & Demultiplexer
MUX, Digital Switch, Multi-Switch, Data Selector
Route the bus data to one of m destinations
Connect 2n points to a single point
Z = A' D0
+ A D1
Z = B’A’ D0
+ B’A D1
+ BA’ D2
+ BA D3
Z = C’B’A’ D0
+ C’B’A D1
+ C’BA’ D2
+ C’BA D3
+ CB’A’ D4
+ CB’A D5
+ CBA’ D6
+ CBA D7
2:1
Mux
D0
D1
A
Z
B
A
Z
4:1
Mux
D0
D1
D2
D3
C
B
Z
8:1
Mux
A
D0
D1
D2
D3
D4
D5
D6
D7
EN
SEL
D0
Dn-1
Y
Enable
Select
n
n
Data
n
2026-03-21

## Slide 65: Logic design with MUX
Lookup Table
F(A,B,C) = m0 + m2 + m6 + m7
8:1
MUX
0
1
2
3
4
5
6
7
S2 S1 S0
S1 S0
4:1
MUX
0
1
2
3
A
0
0
0
0
1
1
1
1
B
0
0
1
1
0
0
1
1
C
0
1
0
1
0
1
0
1
F
1
0
1
0
0
0
1
1
C’
C’
0
1
1
0
1
0
0
0
1
1
A
B
C
F
A
B
C’
C’
0
1
F
2n-1:1 MUX can implement any function of less than n variables

## Slide 66
EN
A
B
C
D0
D1
D2
D3
D4
D5
D6
D7
Y
Y
74x151
Y
X
W
F = (W,X,Y,Z)(0,1,3,7,9,13,14)
Y
WX
00 01 11 10
0
1
Exercise
YZ
WX
00 01 11 10
00
01
11
10
1
1
1
1
1
1
1
1
0
Z
Z
Z
Z
Z’
0
F
Z
VCC
0
4
12
1
5
13
9
3
7
15
2
6
14
10
8
11
2026-03-21

## Slide 67: HDL for Octal 2-to-1 MUX
condition ？true_expression：false_expression
module Mux8 (
);
endmodule
output[7:0] bus1,
input sel,
input [7:0] data1, data0
assign ;
bus1 = sel ? data1 : data0
0
1
bus1
data1
data0
sel
8
8
8

## Slide 68: HDL for 3-to-1 MUX
HARDWARE!
a
sel
2
b
c
q
module Mux31a ( q, a , b, c, sel ) ;
endmodule
output q;
input a, b, c;
input [ 1:0 ] sel;
always @ ( * )
begin
end
case ( sel )
endcase
0: q = a ;
1: q = b;
2: q = c;
default: q = a;
module Mux31b ( q, a , b, c, sel ) ;
endmodule
output q;
input a, b, c;
input [ 1:0 ] sel;
always @ ( * )
begin
end
a
c
sel[1]
b
sel[0]
q
0
1
0
1
No priority
Priority!
if ( sel[0] == 1 ) q = b;
else if ( sel[1] == 1 ) q = c;
else q = a;
reg q;
reg q;
Assigned in Procedural Block
Default alternative
Else alternative
Assigned in Procedural Block

## Slide 69: Examples for Combinational Digital Circuit Design
Multiplexer/Demultiplexer
Decoder/ Encoder
Parity Generator/Checker
Operator
Chap1.3，1.4，4.2
Chap4.7
2026-03-21

## Slide 70: Decoder and Encoder
  Multiple-Input, Multiple-Output Logic Circuit
  Translate one code to another code. Normally used case:
      Output Code of Decoder has More bits than its Input Code
      Output Code of Encoder has Fewer bits than its Input Code
  Enable Inputs must be Asserted to perform Normal Mapping Function
Input
Code
Output
Code
Enable Inputs
1-out-of 2n
Map
Input
Code
Output
Code
Enable Inputs
n-bit Binary
Decoder
1-out-of 2n
Encoder
n-bit Binary
Map

## Slide 71: Binary Decoder
2-to-4
Decoder
Y0
Y1
Y2
Y3
I0
I1
EN
0 X X 0 0 0 0
1 0 0 0 0 0 1
1 0 1 0 0 1 0
1 1 0 0 1 0 0
1 1 1 1 0 0 0
Inputs
EN I1 I0
Outputs
Y3 Y2 Y1 Y0
1.Truth Table
Y0 = EN · ( I1’ · I0’ )
Y1 = EN · ( I1’ · I0 )
Y2 = EN · ( I1 · I0’ )
Y3 = EN · ( I1 · I0 )
2.Logical expression
3. Schematic and logic symbol
1 X X 1 1 1 1
0 0 0 1 1 1 0
0 0 1 1 1 0 1
0 1 0 1 0 1 1
0 1 1 0 1 1 1
Inputs
G_L B A
Outputs
Y3_L Y2_L Y1_L Y0_L
Truth Table
Y0
Y1
Y2
Y3
G
A
B
G_L
A
B
Y0_L
Y1_L
Y2_L
Y3_L
Y0
Y1
Y2
Y3
G
A
B
2-to-4
Decoder
2-to-4
Decoder
How about the Logical expression?
Y0
Y1
Y2
Y3
G
A
B
2-to-4
Decoder
Negative logic
2026-03-21

## Slide 72
Please give the truth table of 3-to-8 Decoder
input |  | output
G1 G2A_L G2B_L | C B A | Y7_L Y6_L Y5_L Y4_L Y3_L Y2_L Y1_L Y0_L
0 X X | X X X | 1 1 1 1 1 1 1 1
X 1 X | X X X | 1 1 1 1 1 1 1 1
X X 1 | X X X | 1 1 1 1 1 1 1 1
1 0 0 | 0 0 0 | 1 1 1 1 1 1 1 0
1 0 0 | 0 0 1 | 1 1 1 1 1 1 0 1
1 0 0 | 0 1 0 | 1 1 1 1 1 0 1 1
1 0 0 | 0 1 1 | 1 1 1 1 0 1 1 1
1 0 0 | 1 0 0 | 1 1 1 0 1 1 1 1
1 0 0 | 1 0 1 | 1 1 0 1 1 1 1 1
1 0 0 | 1 1 0 | 1 0 1 1 1 1 1 1
1 0 0 | 1 1 1 | 0 1 1 1 1 1 1 1
LSB
MSB
EN
A
B
C
G1
G2A
G2B
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
74LS138
Enable
Y6_L=(C·B·A’)’
m6’=M6
Exercise

## Slide 73: Logic design with Decoder and Gates
Z
Y
X
A
B
C
G1
G2A
G2B
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
74x138
F1
+5V
F1 = (X,Y,Z) (0,3,6,7)
While enable input asserted, Yi = mi’=Mi
= M1 · M2 · M4 · M5
= m1’ · m2’ · m4’ · m5’
F2 =  (X,Y,Z) ( 1, 2, 4, 5 )
F2
LSB
MSB

## Slide 74
Dimension Reduction
A B C
0 0 1
0 1 1
1 0 1
1 1 0
73
A B C D
0 0 1 0
0 1 1 0
1 0 1 0
1 1 0 0
Exercise
Please build the circuit F With only one 3-to-8 Decoder

## Slide 75: Binary Encoder
1 0 0 0 0 0 0 0 0 0 0
0 1 0 0 0 0 0 0 0 0 1
0 0 1 0 0 0 0 0 0 1 0
0 0 0 1 0 0 0 0 0 1 1
0 0 0 0 1 0 0 0 1 0 0
0 0 0 0 0 1 0 0 1 0 1
0 0 0 0 0 0 1 0 1 1 0
0 0 0 0 0 0 0 1 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7
A2 A1 A0
This 8-to-3 Encoder is the exact opposite of a decoder.
only one input will be asserted at a time (Guarantee).
A0 = I1 + I3 + I5 + I7
A1 = I2 + I3 + I6 + I7
A2 = I4 + I5 + I6 + I7
………..
How to deal with low level input?
How to deal with multiple requests?
---more than One Inputs are asserted
0 1 1 1 1 1 1 1 0 0 0
1 0 1 1 1 1 1 1 0 0 1
1 1 0 1 1 1 1 1 0 1 0
1 1 1 0 1 1 1 1 0 1 1
1 1 1 1 0 1 1 1 1 0 0
1 1 1 1 1 0 1 1 1 0 1
1 1 1 1 1 1 0 1 1 1 0
1 1 1 1 1 1 1 0 1 1 1
I0 I1 I2 I3 I4 I5 I6 I7
A2 A1 A0

## Slide 76
Priority Binary Encoder
input | output
EI_L I0_L I1_L I2_L I3_L I4_L I5_L I6_L I7_L | A2_L A1_L A0_L GS_L EO_L
1 x x x x x x x x | 1 1 1 1 1
0 x x x x x x x 0 | 0 0 0 0 1
0 x x x x x x 0 1 | 0 0 1 0 1
0 x x x x x 0 1 1 | 0 1 0 0 1
0 x x x x 0 1 1 1 | 0 1 1 0 1
0 x x x 0 1 1 1 1 | 1 0 0 0 1
0 x x 0 1 1 1 1 1 | 1 0 1 0 1
0 x 0 1 1 1 1 1 1 | 1 1 0 0 1
0 0 1 1 1 1 1 1 1 | 1 1 1 0 1
0 1 1 1 1 1 1 1 1 | 1 1 1 1 0
A2
A1
A0
EI
74x148
I7
I6
I5
I4
I3
I2
I1
I0
GS
EO
5
4
3
2
1
13
12
11
10
6
7
9
14
15
The GS_L Output is invalid if all inputs are invalid or EI_L is invalid.
The EO_L Output is valid only if all inputs are invalid.
H7 = I7_L
H6 = I6_L + I7_L’
H5 = I5_L + I6’_L + I7’_L
…
H0 = I0_L +I1_L’ + …+I6_L’ + I7_L’
A2_L = H4 · H5 · H6 · H7
A1_L = H2 · H3 · H6 · H7
A0_L = H1 · H3 · H5 · H7
EI_L is implied.

## Slide 77
module decoder3_8 (
);
always @( )
if( )
case( )
endcase
else
endmodule
input G1,G2A_L,G2B_L, input C, B, A,
output reg[7:0] Y_L
*
G1 & ~G2A_L & ~G2B_L
{C,B,A}
0: Y_L = 8'b11111110;
1: Y_L = 8'b11111101;
2: Y_L = 8'b11111011;
3: Y_L = 8'b11110111;
4: Y_L = 8'b11101111;
5: Y_L = 8'b11011111;
6: Y_L = 8'b10111111;
7: Y_L = 8'b01111111;
default: Y_L = 8'b11111111;
Y_L=8'b11111111;
HDL for 3-8 Decoder
module decoder2_4(I0,I1,EN,Y0,Y1,Y2,Y3);
input I0, I1, EN;
output Y0, Y1, Y2, Y3;
endmodule
module decoder2_4(I0,I1,EN,Y0,Y1,Y2,Y3);
input I0, I1, EN;
output Y0, Y1, Y2, Y3;
endmodule
行为描述风格
A
B
C
G1
G2A
G2B
Y0
Y1
Y2
Y3
Y4
Y5
Y6
Y7
结构描述风格
数据流
描述
风格
I1N
I0N
U5
U3
U4
U6
U1
U2
not U1(I0N, I0),
U2(I1N, I1);
and U3(Y0, EN, I0N, I1N),
U4(Y1, EN, I0, I1N),
U5(Y2, EN, I0N, I1),
U6(Y3, EN, I0, I1);
wire I0N, I1N;
assign I0N = !I0;
assign I1N = !I1;
assign Y0 = !(I0N & I1N & EN);
assign Y1 = !(I0N & in1 & EN);
assign Y2 = !(wire2 & in0 & EN);
assign Y3 = !(in0 & in1 & EN);
wire I0N, I1N;

## Slide 78: HDL for 4-2 Encoder
module Code42( F, I ) ;
endmodule
always @ ( * )
begin
end
HARD-WARE!
F0
I1
I0
I2
I3
F1
always @ ( * )
begin
if (I[3]) t= 2’b11 ;
else if (I[2]) t = 2’b10 ;
else if (I[1]) t = 2’b01 ;
else t = 2’b00 ;
end
No priority
Priority!
output [ 1:0 ] F;
input [ 3:0 ] I;
assign F = t ；
, en);
input en;
reg [1:0] t;
case ( I )
1: t = 0 ;
2: t = 1 ;
4: t = 2 ;
8 : t = 3 ;
default: t = 0 ;
endcase
en ? t : 2’bz;
z: High impedance
en

## Slide 79: The synthesis results

## Slide 80: Examples for Combinational Digital Circuit Design
Multiplexer/Demultiplexer
Decoder/ Encoder
Parity Generator/Checker
Operator
Chap1.3，1.4，4.2
Chap4.7
2026-03-21

## Slide 81: Parity-Checking Applications
Detect errors in the transmission and storage process.
A
EVEN
ODD
74x280
H
I
A
EVEN
ODD
74x280
H
I
DB[0:7]
DB[0:7]
ERR
Transmitter
Receiver
9bits
Parity Generator
Parity Checker
Which logic operation we have learned can used for parity circuit?
2026-03-21

## Slide 82: Parity Circuit
Even-Parity Gen: Output is 1 if the number of the input 1 are odd.
Odd-Parity Gen: Output is 1 if the number of the input 1 are even.
A0  A1  …  An =
1
0
if the number of variable ‘1’ is odd
if the number of variable ‘1’ is even
A0
A1
A2
A3
An
EVEN
A0
A1
A2
A3
An-1
An
EVEN
Tree Structure
Daisy-chain Structure
How can we get an odd-parity circuit?
Invert the output of even-parity circuit
2026-03-21

## Slide 83: Review of XOR and XNOR
AB=(A⊙B)’ AB’=A⊙B AB=A⊙B’
Any two signals( inputs or output) of an XOR or XNOR gate could be complemented without changing the resulting logic function.
F=AB
A
B
F
A
B
F
A
B
F
A
B
F
F=A’B’
F=(A’B)’
F=(AB’)’
2026-03-21

## Slide 84: Comparator design
Comparator: Check if two Binary words are equal
Magnitude Comparator: Compare their magnitude (Greater than, Equal, Less than)
How to build a 1-bit Comparator?
A
B
A
B
DIFF
EQ
Chap4.9
2026-03-21

## Slide 85: Exercise
Please Build a N-bit Comparator with 1-bit comparator.
X Y
EQI EQO
A1
B1
AN-1
BN-1
EQN
“1”
X Y
EQI EQO
X Y
EQI EQO
The upper one is a parallel N-bit Comparator.
The lower one is a Serial N-bit Comparator.
The lower structure is cheaper but slower than the upper one.
A
B
EQO
EQI
DIFF
A0
B0
A1
B1
A2
B2
A3
B3
Serial/Iterative/Daisy-chain structure
Paraller/Tree Structure
A0
B0
2026-03-21

## Slide 86: Examples for Combinational Digital Circuit Design
Multiplexer/Demultiplexer
Decoder/ Encoder
Parity Generator/Checker
Operator
Chap1.3，1.4，4.2
Chap4.7
2026-03-21
Chap4.3，4.5

## Slide 87: 1-bit Adder
module Add_full(c_out,sum,a,b,c_in);
endmodule
  CO=XY
  S=X’ Y+XY’
  =X⊕Y
half adder 半加器 |  |  | 
X | Y | CO | S
0 | 0 | 0 | 0
0 | 1 | 0 | 1
1 | 0 | 0 | 1
1 | 1 | 1 | 0
full adder 全加器 |  |  |  | 
X | Y | CI | CO | S
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 1
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 1
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 1 | 1
Logic Symbol
逻辑符号
Truth table
真值表
Logic Function
逻辑表达式
  Verilog code
  HDL语言
module Add_half(c_out, sum, a, b,);
endmodule
  CO=X’YCI+XY’CI+XYCI’+XYCI
  =XY+XCI+YCI
  S=X’Y’CI+X’YCI’+XY’CI’+XYCI
  =X⊕Y⊕CI
input a,b;
output c_out,sum;
and(c_out,a,b);
xor(sum,a,b);
input a,b,c_in;
output c_out, sum;
Add_half P1(w1,w2,a,b);
Add_half P2(w3,sum,w2,c_in);
or P3(c_out,w1,w3);
wire w1,w2,w3;
Schemitic
电路原理图
P1
P2
P3
W1=XY
W2= X⊕Y
W3=W2 CIN
Full
Adder
X
Y
Cout
Sum
Full
Adder
X
Y
Cin
Cout
Sum
2026-03-21

## Slide 88: A 4-bit ripple-carry adders
87
the longest path

## Slide 89: Structure of addition/subtraction
The same function can be achieved by replacing the multiplex and inverter with an XOR gate.

## Slide 90: 4-bits Signed Adder
module Adder4 ( A, B, Cin, S, Cout , Ovout ) ;
endmodule
Adder4
A
B
4
4
Cin
4
Cout
S
How about the circuit after synthesis?
Check it.
Operator Definition
input [ 3:0 ] A, B;
input Cin;
output [ 3:0 ] S;
output Cout , Ovout ;
assign {Cout, S} = A + B + Cin ;
assign OVout= (A[3]==B[3]) && (S[3] !=A[3]);

## Slide 91: 4-bit Add_Suber
module AddSub ( input S,
input [3:0] A, B,
output reg [3:0] F,
output reg Unsigned_Overflow, Signed_Overflow );
reg [4:0] TempF;
assign F = TempF[3:0];
assign Unsigned_Overflow = TempF[4];
always @ ( * ) begin
if (S == 0) begin
TempF = {1'b0,A} + {1'b0,B};
Signed_Overflow = ((!A[3]) & (!B[3]) & (TempF[3])) + ((A[3]) & (B[3]) & (!TempF[3])); end
else begin
TempF = {1'b0,A} - {1'b0,B};
Signed_Overflow = ((A[3]) & (!B[3]) & (!TempF[3])) + ((!A[3]) & (B[3]) & (TempF[3])); end
end
endmodule
// addition
// zero extend A and B
// = MSB of A'B'F + ABF'
// = MSB of AB'F' + A'BF
// subtract
// zero extend A and B
// select 0=add, 1=subtract
90

## Slide 92: 8-bit ALU
module ALU8 (
);
endmodule
output reg [7:0] ALUout
input [7:0] left, right,
input [1:0] mode,
always @(*)
begin
end
case (mode)
0: ALUout = left + right;
1: ALUout = left - right;
2: ALUout = left & right;
3: ALUout = left | right;
default: ALUout = 8'bX;
endcase
Default alternative if mode contains anything but 1s and 0s
The Declaration of ALUout both as output and reg: Because of assigning it within a Procedural Block
x: undetermined

## Slide 93
Design & Analysis of Combinational Circuits
  Digital Circuit Design is:
  To descript and simplify the function
    truth table/ K map
    logical algebra expressions/equations
    CSOP/Minterm list, CPOS/Maxterm list, MSOP, MPOS
    circuit diagram (Schematic at Module level, RTL level, etc. )
    timing diagram (Waveform)
    Hardware Description Language code (VHDL, Verilog, etc.)
  To realize the hardware
    gates or other devices
    Programmable Logic Devices
    Application Special Integrate Circuit
Digital Circuit Analysis is:
  To determine the behavior of the circuit
  To verify the correctness of the circuit
  To assist in converting the circuit to a different form

## Slide 94
Design & Analysis of Combinational Circuits
  Digital Circuit Design is:
  To descript and simplify the function
    truth table/ K map
    logical algebra expressions/equations
    CSOP/Minterm list, CPOS/Maxterm list, MSOP, MPOS
    circuit diagram (Schematic at Module level, RTL level, etc. )
    timing diagram (Waveform)
    Hardware Description Language code (VHDL, Verilog, etc.)
  To realize the hardware
    gates or other devices
    Programmable Logic Devices
    Application Special Integrate Circuit
Digital Circuit Analysis is:
  To determine the behavior of the circuit
  To verify the correctness of the circuit
  To assist in converting the circuit to a different form
CAD：Computer Aided Design
EDA：Electronic Design Automatic

## Slide 95: VHDL vs. Verilog
Government Developed in 1981 | Commercially Developed in 1985
Ada based | C based
Strongly Type Cast | Mildly Type Cast
Case-insensitive | Case-sensitive
Difficult to learn | Easier to Learn
  VHDL is an acronym for :
  VHSIC (Very High Speed Integrated Circuit) Hardware Description Language
HDLs is used to describe a HARDWARE!
They are quite different with the tradition program language!
Chap1.4

## Slide 96: TOP-DOWN Design
Control Module
Datapath Module
PART 1
(combination)
PART 2
(combination)
PART 3
(sequential
FSM)
PART 1
(combination)
PART 2
(combination)
PART 4
(Register)
PART 3
(combination)
PART 5
(Counter)
Digital circuit
Top-level module
port-function
Interconnect
PART 4
(sequential
FSM)
Interconnect
Interconnect
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function
module
port-function

## Slide 97: Basic Verilog Modeling
module is a most basic building block of a design.
port_mode port_name1;
port_mode port_name2;
…………
circuit functionality describes an implementation of the corresponding module.
port declarations describes the interface of the component, i.e. input and output ports.
assign statements;
always @(sensitive signals list)
begin
functionality code
end
module module_name (port_name1,_port_name2, …);
port declarations
circuit functionality
endmodule
Interconnect declarations
wire interconnect_name1;
wire interconnect_name1;
…………

## Slide 98: Fundamental rules of Verilog
module MultiplexerC (w，a, b, s);
output reg w;
input a，b，s;
wire m;
assign m = a+b;
always @(*)
begin
if (s) w = b;
else w = m;
end
endmodule
module name
reserved words
lowercase
Semicolon
No Semicolon
Continuous Assignment statement is used if the unit is simple
Procedural Block(always)
statement with sensitivity list is used when the unit is too complex
Declare port and inter-connect signal
module ports
The signal assigned in always block should be ‘reg’ type

## Slide 99: Verilog Design Styles
Components and
interconnects
structural
behavioral
(sequential)
Subset most suitable for synthesis
Testbenches
I1
I2
Y
I1
I2
Y
U1_OUT
module structural (Result, A, B, C);
output Result;
input A, B, C;
wire U1_OUT;
xor U1(U1_OUT,A,B); xor U2(Result,U1_OUT,C);
endmodule
module behavioral (Result, A, B, C);
output reg Result;
input A, B, C;
always @ (*)
begin
Result = (A ^ B) ^ C;
end
endmodule
dataflow
Concurrent statements
module dataflow (Result, A, B, C);
output Result;
input A, B, C;
assign Result = (A ^ B) ^ C;
endmodule
Chap1.2

## Slide 100: Interconnections
ALU8 U1 ( .left(Inbus), .right(ABinput),
.mode(Function), .ALUout(Outbus) );
Mux8 U2 ( .sel(select_source), .data1(Aside), .data0(Bside), .bus1 (ABinput));
Instantiated
u1 and u2 : Instance Names
module ALU8 (input [7:0] left, right,
input [1:0] mode,
output reg [7:0] ALUout );
……..
endmodule
module Mux8 ( input sel,
input [7:0] data1, data0,
output[7:0] bus1 );
……..
endmodule
Defined Port
Real connection
Defined
Defined
ALU8 U1 ( Inbus, ABinput, Function, Outbus );
Ordered Port Connection

## Slide 101: Organization of Center Processor Unit
2026-03-21
Decoder
Parity Generator
Parity Checker

## Slide 102
2026-03-21
101
THE END OF Topic2-1
Digital Logic Design and Application
Topic 2 - Principles for digital design Yan Bo
School of Information & Communication Engineering, UESTC
Email: yanboyu@uestc.edu.cn

## Slide 103: Required reading
  Digital System Design with Verilog & VHDL
2nd Edition，Enoch O.Hwang著，阎波 朱晓章 姚毅改编
      Chapter 2, Fundamentals of Digital Circuit
      Chapter 3, Combinational Circuits
      Chapter 4, Standard Combinational Components
  Digital Design: Principles and Practices
  4th Edition, John F. Wakerly
      Chapter 4, Combinational Logic Design Principles
      Chapter 5, Combinational Logic Design Practices
  数字逻辑设计及应用
  姜书艳等，电子科技大学出版社
      Chapter 3 , Basis of Logic Algebra
      Chapter 5, Combinational Logic Circuit Design
  数字集成电路与系统设计
  李广军、郭志勇等，电子工业出版社
      Chapter 4 , Verilog HDL基础
      Chapter 5, 数字逻辑电路的Verilog RTL建模与设计

## Slide 104: Homework2-1
P17 1.9、1.10
P59 2.4（ b ）、 2.5（ c ）、2.7（ d ）、
2.10（ c ）、2.12（ c ）、2.14（ d ）
2.27 （a, d）、 2.28（ c ） 、2.34、2.35
P106 3.1（ d ） 、 3.2（ d ） 、3.4（a, e） 、
3.11、3.17（ b ） 、3.23（c, f）、
3.26（a）、3.36
P151 4.2、4.25 、4.28、4.32

## Slide 105: Homework2-1（ Additional questions ）
2. Please finish the function as below:
1) Consider the 8-to-1 MUX as a single component shown here
2) Use 1 pcs 74LS138 to finish the same F(x,y,z), other basic gates are also allowed to be used.
F (x, y, z) = x'y'z' + x'yz' + xy'z + xyz' + xyz.
1. Using Karnaugh maps, find a minimal SOP expression and a minimal POS expression for each of the following logic functions. Indicate the distinguished 1-cells (or 0-cells) in each map.
(a) F= Sx,y,z(1,3,5,6,7)
(b) F= SW,X,Y ,Z(0,1,2,8,11)+ d(3,9,15)