## Slide 1: Digital Logic Design and Application
Lab Course 5
Lecturer:
TA:
Lab Room:

## Slide 2: Fundamental
Digital Logic + Computer Architecture
Verilog Language
Tools
  EDA software: Vivado 2017.1
  Evaluation board: EES331
Lab report submitted
  e-file name: report no. + student code + name (eg: 1_20xxxxxx_Alex)
  send to email: same as the homework
  cut-off time: report1 : before lab3 （before 14, May）
  report2 : 1 week after lab5（before 10, May ）

## Slide 3: Grading
Assessment
Lab1 10% + Lab2 20% + Lab3 20% + Lab4 20% + Lab5 10% + Report1 5% + Repor2 15%
And for each lab:
  Pre-Lab preparation and Performance in laboratory (65%)
  Laboratory experimental reports (35%)

## Slide 4: Note
  Please save the screenshots of the code, simulation result, etc.
  You will need them to write the Lab_report.

## Slide 5: Content
EDA tools
Datapath Design
Controller Design
CPU Integration
CPU Verification and Improvement
  Enlarge your own instruction set (for example: add several instructions) and modify the datapath & controller modules based on the new instruction set
  Compose a better testbench and do verification again
  Describe your work as clearly as possible in your lab report2

## Slide 6: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | Mov R1 #02 Mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | Add R1 #08 Add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0110 0111 | 11 01 | xx 10 | 00000011 xxxxxxxx | And R1 #03 And R1 R2 | R3<= (R3) bit_and (3) R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 7: 1. Create New Hardware Project
Follow the steps of lab1.ppt to create New Hardware Project.

## Slide 8
2. Create New Source File -step1
Follow the steps of lab4.ppt to create files in the code folder like this

## Slide 9
2. Create New Source File -step2
Refer to the next page to combine cpu and rom in top_cpu.v

## Slide 10
2. Create New Source File -step3
CPU
ROM
clk
rst
16
ins
en_ram_out
addr
16
en_ram_in
system_top

## Slide 11
2. Create New Source File -step4
A ROM (Read-only memory), with instructions editable in design phase.
Design your program according to the equation below.
Be aware that data exceeding the defined address is unknown.
[8-(2+1) ]|(2+1)+1

## Slide 12
3. Create the ILA IP core (Integrated Logic Analyser)

## Slide 13
3. Create the ILA IP core
Step-1
1. Left-click

## Slide 14
3. Create the ILA IP core
Step-2
1. Left-click
1. Input name to search IP cores
2. Double click

## Slide 15
3. ADD
IP CORE
-step2-2
1. Module’s name
2. Input parameter

## Slide 16
3. ADD
IP CORE
-step2-3
1. Input parameter

## Slide 17
3. ADD
IP CORE
-step2-4
1. Left click

## Slide 18
3. ADD
IP CORE
-step2-5
Ensure these signals are connected to probes.
We need to pay attention to the signals q0, q1, q2, and q3.
reg_group

## Slide 19
3. Do Synthesis and get the circuit
Follow the steps of lab1.ppt to do Synthesis and get the circuit

## Slide 20
Add tb_top_cpu.v to the project as simulation source
4. Create Simulation Source
File
Define clk
Define rst

## Slide 21
5. Create the constraint
Copy contents in PINS_SET.txt to this window

## Slide 22
6.Connect FPGA Target Board With Computer
1. Put all switch(17 ) to ON
2.Connect J3(2) and USB port of computer with USB cable
3.Power on with switch (7)
4.system reset L18(13)

## Slide 23
7. program device
Follow the steps of lab1.ppt

## Slide 24
8. Run ila to see the data in the registers
-step1
2. Add signals
1. Select the ila
3. Select all
4. Click ok

## Slide 25
8. Run ila to see the data in the registers
-step2
2
1
3
Add Trigger Signal

## Slide 26
9. Run ila to see the data in the registers
-step3
1. Set Trigger Condition
3.Start Trigger
2.Press and hold the reset button on the board !!!!!!
4.Release the reset button!!!!!!

## Slide 27: Some other ideas for Instruction Set
Memory access instructions
Ldr, Str
Conditional branch instructions
Jz, Jnc, …
Other data operation instructions
  Xor, Cmp…..
  Acc (add 1 to N)

## Slide 28: Digital Logic Design and Application
Lab Course 5
~~End~~