## Slide 1: Digital Logic Design and Application
Lab Course 3
Lecturer:
TA:
Lab Room:

## Slide 2: Grading
Assessment
Lab1 10% + Lab2 20% + Lab3 20% + Lab4 20% + Lab5 10% + Report1 5% + Repor2 15%
And for each lab:
  Pre-Lab preparation and Performance in laboratory (65%)
  Laboratory experimental reports (35%)

## Slide 3: Requirements
1. Understand the function of the control unit in CPU.
2. Consider about the controller’s STG according to the ISA.
3. Finish the state_transition module based on the given codes .
4. Simulate and check the results.

## Slide 4: Note
  Please save the screenshots of the code, simulation result, etc.
  You will need them to write the Lab_report.

## Slide 5: Content
EDA tools
Datapath Design
Controller Design
  Understand the STG for control_unit ;
  Design state_transition component;
  Coding, Synthesis and simulate state_transition component;
CPU Integration
CPU Verification and Improvement

## Slide 6: CPU Organization
CPU
Control
Unit
Datapath
state_
transition
Control Unit
ALU &
ALU MUX
Registers
Datapath
PC
IR

## Slide 7: data_path.v
reg_group1
module data_path
register.v
module register
data_path.v
alu_mux1
alu1
pc1
reg_group.v
module reg_group
alu_mux .v
module alu_mux
alu.v
module alu
pc.v
module pc
register.v

## Slide 8
alu_mux alu_mux1 (
. rst (rst)
. en_in (en_in ),
. rd_q (rd_q) ,
. rs_q (rs_q),
. offset (offset),
.alu_in_sel (alu_in_sel),
.alu_a (alu_a ),
.alu_b (alu_b)
);
alu alu1 (
.alu_a (alu_a),
.alu_b (alu_b),
……
);
module alu_mux (
rst,
en_in,
offset,
rd_q,
rs_q,
alu_in_sel,
alu_a,
alu_b
);
alu_mux .v
设计名
例化名
模块的引脚名
与模块引脚相连的信号
名
datapath .v
ALU
reg
_
group
16
alu
_
a
16
alu
_
b
4
offset
alu
_
in
_
sel
alu
_
out
16
reg
_
en
rd
_
q
mux
rs
_
q
16
16
2
rd
3
alu
_
func
2
rs
D
alu
_
mux
16
8

## Slide 9: Top structure of our CPU
Data
path
Control
Unit
regs control signals
CPU
reg group
alu
pc
alu_mux
ir
state
transition
pc control signals
en_group, reg_en,…
Opcode
en_pc, pc_ctrl,…
Other signals
alu control signals
alu_func,…
alu_mux control signals
alu_in_sel,…

## Slide 10: Instruction Set
Opcode | Rd | Rs | Imme | assembly | function
4bit | 2bit | 2bit | 8bit |  | 
0000 0001 | 01 10 | xx 01 | 00000010 xxxxxxxx | Mov R1 #02 Mov R2 R1 | R1<= 2 R2<=(R1)
0010 0011 | 01 01 | xx 10 | 00001000 xxxxxxxx | Add R1 #08 Add R1 R2 | R1<=(R1)+8 R1<=(R1)+(R2)
0101 | 01 | 10 | xxxxxxxx | Sub R1 R2 | R1<=(R1)-(R2)
0111 | 01 | 10 | xxxxxxxx | And R1 R2 | R1<= (R1) bit_and (R2)
1001 | 01 | 10 | xxxxxxxx | Or R1 R2 | R1<=(R1) bit_or (R2)
1010 | xx | xx | 00000001 | Jump #01 | PC<= 1
Opcode supports 16 instructions. So you can add other instructions, like shift, multiplication.
Rd and Rs can be expressed in 2 bits that means you can operate 4 registers.
Immediate data is expressed in 8 bits.

## Slide 11: State transition

## Slide 12: Control signals & state signal meaning
Control signals
reg_group
en_group: enable signal, whether get datas from register group
reg_en: enable signal, means whether enable 4 registers to store datas to registers
alu_mux
alu_in_sel: see PPT for the last class
alu
alu_in_func: see PPT for the last class
pc
en_pc: enable signal, whether enable pc unit
pc_ctrl: mux signal, if pc_ctrl = 00 means pc_out <= pc_out ;
if pc_ctrl = 01 means pc_out <= pc_out +1;
if pc_ctrl = 10 means pc_out <= offset;
State signal
alu_out：status signal, whether the alu output is ready

## Slide 13
Controller Design

## Slide 14: 1. Create New Hardware Project
Follow the steps of lab1.ppt to create New Hardware Project

## Slide 15
2. Create New Source File -step1
Add files in the code folder as following steps.

## Slide 16
Click here
2. Create New Source File -step2

## Slide 17
2. Create New Source File -step3
Refer to the next page to complete the state_transition module.

## Slide 18
2. Create New Source File -step4

## Slide 19
3. Do Synthesis and get the circuit
Follow the steps of lab1.ppt to do Synthesis and get the circuit

## Slide 20
Copy the content in tb_state_transition.v to this window, and complete the code
4. Create Simulation Source
File -step1
tb_state_transition

## Slide 21
4. Create Simulation Source
File
-step2
1.Right- click
2.Click

## Slide 22
4. Create Simulation Source
File
-step3
Run simulation and observe the variation of signals. Make sure all of these are right.

## Slide 23: Digital Logic Design and Application
Lab Course 3
~~End~~